## Slide 1: Arduino Mega 2560

## Slide 2: Prepared by
Amgad Magdy Fathy Sayed Ahmed
  Academic No. 1900113
    Section No. 1

## Slide 3: Agenda
Overview
Technical Specification
Reference(Datasheet)

## Slide 4: Overview

## Slide 5: What’s Arduino Mega 2560
Arduino Mega 2560 is an exemplary development board dedicated for building extensive applications as compared to other maker boards by Arduino. The board accommodates the ATmega2560 microcontroller, which operates at a frequency of 16 MHz . The board contains 54 digital input/output pins, (of which 15 can be used as PWM outputs), 16 analog inputs, 4 UARTs (hardware serial ports), a USB connection, a power jack, an ICSP header, and a reset button.

## Slide 6: Technical Specification
Crystal
oscillator

## Slide 7
Microcontroller | ATmega2560
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limit) | 6-20V
Digital I/O Pins | 54 (of which 15 provide PWM output)
Analog Input Pins | 16
DC Current per I/O Pin | 20 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 256 KB of which 8 KB used by bootloader
SRAM | 8 KB
EEPROM | 4 KB
Clock Speed | 16 MHz
LED_BUILTIN | 13
Length | 101.52 mm
Width | 53.3 mm
Weight | 37 g

## Slide 8: Board
ATmega2560 Processor
  Up to 16 MIPS Throughput at 16MHz
  256k bytes (of which 8k is used for the bootloader)
  4k bytes EEPROM
  8k bytes Internal SRAM
  32 × 8 General Purpose Working Registers
  Real Time Counter with Separate Oscillator
  Four 8-bit PWM Channels
  Four Programmable Serial USART
  Controller/Peripheral SPI Serial Interface

## Slide 9: Board
ATmega16U2
Up to 16 MIPS Throughput at 16 MHz
16k bytes ISP Flash Memory
512 bytes EEPROM
512 bytes SRAM
USART with SPI master only mode and hardware flow control (RTS/CTS)
Master/Slave SPI Serial Interface

## Slide 10: Board
Power
USB Connection
External AC/DC Adapter

## Slide 11: Board
I/O Pinouts
54 digital I/O pins.
16 analog input pins.
15 PWM Output

## Slide 12: Reference
https://docs.arduino.cc/hardware/mega-2560/

## Slide 13: THANK YOU